| NSSP Standardized Shellfish Processing Plant Inspection Form |
| --- |
| Agency Name: | Date |
| Type of Inspection | ( Certification ( Pre-operational ( Routine ( Follow-up ( Standardization |  |
| Dealer Name: |  | Certification Number |
| Dealer Address: |  |  |
|  | Hazard Analysis Critical Control Point (HACCP) |  |
| 1. | HACCP Plan Yes ( No ( Required for Certification |
| 2. | Plan Elements Identified and Adequate | (/( NA | Code |  | (/( NA | Code |
|  | (a) Hazards |  | O | (e) Critical Control Points |  | K |
|  | (b) Records |  | O | (f) Monitoring |  | K |
|  | (c) Critical Limits |  | K | (g)Verification Procedures |  | O |
|  | (d) Name, Address, Signed and Dated |  | O | (h) Corrective Action if identified |  | K |
| 3. | HACCP Training | Yes ( No ( | Code O |  |
| 4. | Plan Implementation | Corrective Actions Recorded (K) Verification Procedures (K) (Signature) Monitoring Procedures (K) Records: Accurate/ Maintained (K) Format (O) |  |
|  |  | Initialed/Dated (O) Firm’s Name on record (O) | (/( NA | Code |
|  | (a) | Receiving |  |  |  |
|  | (b) | Shellstock Storage |  |  |  |
|  | (c) | Processing |  |  |  |
|  | (d) | Shucked Meat Storage |  |  |  |
|  | (e) | Other Critical Limits |  |  |  |
| 5. | Approved Source Control Failure |  | C |
| 6. | Time/Temperature Control Failure |  | C |
| 7. | Other Critical Control Failure |  | C |
|  | Sanitation Items | Citation | (/( | Code |
| 8. | Safety of water for processing and ice production | .02A |  |  |
| 9. | Condition and cleanliness of food contact surfaces | .02B |  |  |
| 10. | Prevention of cross-contamination | .02C |  |  |
| 11. | Maintenance of hand-washing, hand sanitizing, and toilet facilities | .02D |  |  |
| 12. | Protection from adulterants | .02E |  |  |
| 13. | Proper labeling, storage, and use of toxic compounds | .02F |  |  |
| 14. | Control of employees with adverse health conditions | .02G |  |  |
| 15. | Exclusion of pests | .02H |  |  |
| 16. | Sanitation Monitoring and Records |  |  | S(K/O) |
|  | Additional Model Ordinance Requirements | Citation | (/( | Code |
| 17. | Plants and Grounds | .03A |  |  |
| 18. | Plumbing and related facilities | .03B |  |  |
| 19. | Utilities | .03C |  |  |
| 20. | Disposal of other waste | .03D |  |  |
| 21. | Equipment condition and cleaning, maintenance, and construction of non-food contact surfaces | .03E |  |  |
| 22. | Shellfish storage and handling | .03F |  |  |
| 23. | Heat shock | .03G |  |  |
| 24. | Supervision | .03H |  |  |
| 25. | Transportation (To include only the person shipping) | IX.05 |  | K |
| 26. | Labeling and Tagging | X.05,.06,.07 |  | S (K/O) |
| 27. | Shipping Documents and Records / Written Recall Procedures | X.08, .03 |  | K |
| Dealer’s Signature | Inspector’s Signature |

[Code: Critical -C; Key-K; Swing-S; Other-O]           ISSC Form 93-01(A) revised ISSC 2007                 Page  1  of  ___

# Effective Date:  11/17/2008